## Slide 1: Interacting with Smart Things
Internet of Things
Module lead: Dr Mir Seyedebrahimi

## Slide 2: Recap: IoT scope’s clarification
Clarification of the IoT scope that is considered for this module:
IoT is a network of identifiable and interacting Things
Networking
Embedded system devices

## Slide 3: Recap: IoT architecture reference
Clarification of the IoT reference model that is considered for this module:
Communication Protocols
Device/Thing/SmartThing
Gateways/Aggregators/Local servers
Analytics/Services
Portals/Dashboards/APIs
Device/ID Managers
Access Managers

## Slide 4: Recap: Reference model - a practical view
Things
Smart Devices
uC
Gateway
Local process/analytics
Devices
Devices
uC
Things
Remote server/cloud services
Analytical tools and user portals
Identification and security management

## Slide 5: Recap: IoT protocol stack
Clarification of the IoT protocol stack that is considered for this module:

## Slide 6: Recap: solution development approach
Within the scope of this module, IoT solutions require the inclusion of the following details:
Physical Entity View: and the exact physical properties of the desired ‘Things’ as much as relevant to the solution
IoT Context View: which is the IoT-related technical details of the solution mainly from end-user device and networking points of view
Information View: which is mainly the description and visualisation of required data sets, objects, their corresponding properties and parameters as well as their inter-relationships

## Slide 7: Recap: Network architecture
So far, we have introduced the first building block of an IoT architecture: the ‘Things’
The second block to build an IoT solution will be the ‘Network Architecture’
Networking aspect of IoT will be initially focused on defining appropriate first 2 layers of IoT protocol stack comprising the connectivity and the addressing points of view
The higher layer protocols and apps then can be defined accordingly (capabilities/performances are dependant on the first two layers’ specifications)

## Slide 8: Continuation of the discussion: ‘Things’ Control methods
Direct Control:
  interact with an object directly through the object itself.
  This is a self-reliant object and not yet to be considered as a connected ‘Thing’
Local Control:
  interact with the ‘Thing’ using a digital or analog interface locally connected to the object.
Remote Control:
  interact with the ‘Thing’ over a network (e.g. an IP network). In most cases, this means interacting with an IoT Registration Server or an IoT Gateway.

## Slide 9: Continuation of the discussion Today’s plan
Today’s work will be mainly a step by step integration of physical objects/Things over the network and corresponding protocols. These include prepacked smart devices and newly created things:
Smart Things:
  that are Registration Server or Home Gateway compatible and can be controlled from a condition-to-actions UI interface
Components:
  that plug into digital or analog slots on a microcontroller (MCU) or single board computer (SBC)
Additionally, it is possible to create Things:
  Things are physical objects and are only bound to the user's imagination
  These can be everyday Things like coffee makers, microwaves or more complex Things like space rovers. The Things are programmable and can interact with Packet Tracer's Environment.
Note: further work with the above features may require programming in JavaScript, Python, or Visua and also to manipulate the components.

## Slide 10: Recap: Cisco Packet Tracer (ver 8.0.0)

## Slide 11: Interacting with Smart Things
Prepacked devices
Programmable elements

## Slide 12: Direct or local control
Or for example through a locally connected switch
Device can be controlled directly

## Slide 13: Remote Control: Home Gateway
Control through Home Gateway

## Slide 14: Remote Control: Registration Server
Control through IoT Registration Server:
Enable the IoT server
Monitor through desktop app

## Slide 15: Accessing IoT Registration Server
Things are accessible through a desktop monitor app or direct browsing the Home gateway or registration server

## Slide 16: Conditional acts
Integrated elements can be monitored, controlled and/or interact based on predefined conditions mainly applied to the selected parameters

## Slide 17: edit programming projects

## Slide 18: Creating Things

## Slide 19: Thing Editor

## Slide 20: Environment Dialog

## Slide 21: Environment Dialog Edit Mode

## Slide 22: APIs
Basic Networking | Package = networking |  | 
Function | Return Type | Description | Example
localIP() | str | Returns the local IP. | ip = localIP()
subnetMask() | str | Returns the subnet mask. | mask = subnetMask()
gatewayIP() | str | Returns the gateway IP. | gateway = gatewayIP()
HTTP Client | Package = http |  | 
Function | Return Type | Description | Example
HTTPClient() | HTTPClient | Creates a HTTP Client. | http = HTTPClient()
open(url) | N/A | Gets an URL. | http.open(“http://www.cisco.com”)
stop() | N/A | Stops the request. | http.stop()
onDone(callback) | N/A | Sets the callback for when the request is done. | def onHTTPDone(status, data): print(data) ... http.onDone(onHTTPDone)
Prepacked library provide access to some major APIs and more can be added through programming feature. Below an example for http that can also be used in a real http and emulation mode

## Slide 23: End of session