## Slide 1: IoT Ecosystem
Internet of Things
Module lead: Dr Mir Seyedebrahimi

## Slide 2: What is IoT?
The term ‘Internet of Things’:
“…describes the pervasive presence of a variety of devices (such as sensors, actuators, mobile phones ..) which, through unique addressing schemes, are able to interact and cooperate with each other to reach common goals.”
So, we consider IoT as:
A network of THINGS which are identifiable and interacting
Source: Peter Marwedel (reading list)

## Slide 3: Things?
Things can be:
Smart buildings and home appliances:
  e.g. washing machines, TVs, fridges, cookers, doors, chairs…
Wearable devices
  e.g. smart watches, smart glasses, rings, clothes
Medical equipment:
  e.g. healthcare monitoring, embedded pills
Industrial tools:
  e.g. robots, monitoring nodes, actuators
Civil engineering structures:
  e.g. bridges, railways …
…
Source: Peter Marwedel, reading list

## Slide 4: What is IoT? A chronological order
IoT initially referred to:
  the introduction of barcodes and Radio Frequency Identification (RFID), helping to automate inventory, tracking and basic identification
Gradually, IoT characterised:
  for connecting sensors, objects, devices, data sources and applications
Recently, IoT has become:
  An icon for 4th industrial revolution (Industry 4.0), which comprise a flexible production solution with full life cycle (from design to production) influenced by IoT and Cyber-Physical Systems. Hyper-connectivity, interoperability and enriched information distribution solutions
Notes: Hyperconnectivity and being connected all the time requires the interoperability to be in place

## Slide 5
Why IoT?
Smart
Lighting
Smart Appliances
Fitness / Healthcare
Portable and Wearable
Electronics
Safer Automotive
Machine to Machine
Industrial Internet
Resource
Management
Smart Farming
Why IoT is helpful?
  Items can express their functionalities and become more intelligent
  Items can be managed in an easier way
  More information become available
Why IoT is becoming more realistic?
  Communication is becoming faster
  Embedded chips are becoming:
          Smaller
          Lower power
          Cheaper (in 2021/22 ?!)
Source: ARM training kit

## Slide 6: Challenges of Internet of Things
Multiple technological enablers required:
  Embedded systems, Communications, Networking, analytical tools etc
Large amount of chips required
  Chips have to become cheaper, smaller
Big data demand
  Large volume of data will be generated, data centre storage needs to be increased, Computation requirement
Power consumption
  Low power chips, longer battery life, and maybe wireless charging…
Security
  Large amount of private data need to be protected
Standards
  Official standards are required, such as network protocol
Source: ARM training kit

## Slide 7: The IoT Opportunity Gap
1 Weiser, Mark (1991) “the Computer for the 21st Century”
Reach
Time
Silos of Things
existing
possible
Current trend shows strong growth and this not new, it’s been around for > 30 years1
Connected things > world population
The IoT Opportunity is much larger than current state and analysts predictions for connected devices (2025):
75 billion?
100 billion?!
Opportunity gap

## Slide 8: Market penetration
CAGR = Compound Annual Growth Rate
This stats is before the Covid impact!

## Slide 9: IoT Growth by Verticals
Verticals: various use cases
And again, this is before the impact of Covid!

## Slide 10: IoT Reference Model
People and Apps
Data acquisition and process
Smart devices, connectivity and mobility
Source: Cisco

## Slide 11: IoT reference model: Architectural perspectives
Communication Protocols
Device/Thing/SmartThing
Gateways/Aggregators/Local servers
Analytics/Services
Portals/Dashboards/APIs
Device/ID Managers
Access Managers
We consider this model for organising our discussion in this module:
Initial teaching topics
Further study and central theme in your assignment
Remaining of the discussions towards the final days

## Slide 12: IoT reference model: Architectural perspective- example
Things
Smart Devices
uC
Gateway
Local process/analytics
Devices
Devices
uC
Things
Remote server/cloud services
Analytical tools and user portals
Identification and security management
System boundaries and communications are considered in this module

## Slide 13: IoT reference model: Networking perspective
A conventional computer network protocol stack comprises:
Process and application
Data presentation and encryption
Inter-host communication
E2E comm. reliability
Path determination and IP
Physical addressing
Media and signal

## Slide 14: IoT reference model: Networking perspective
IoT protocol stack:
Process and application
Data presentation and encryption
Inter-host communication
E2E comm. reliability
Path determination and IP
Physical addressing
Media and signal

## Slide 15: IoT protocol stack further details
Data Protocols (ex: MQTT, CoAP, AMQP, Websocket, Node)
Device Management (ex: TR-069, OMA-DM)
Semantic (ex: JSON-LD, Web Thing Model)
Multi-layer Frameworks (ex: Alljoyn, IoTivity, Weave, Homekit)
Infrastructure (ex: 6LowPAN, IPv4/IPv6, RPL)
Identification (ex: EPC, uCode, IPv6, URIs)
Comms / Transport (ex: Wifi, Bluetooth, LPWAN)
Discovery (ex: Physical Web, mDNS, DNS-SD)

## Slide 16: Technologies that enable IoT
Technologies that enable IoT
  Little Devices and Little Data – embedded devices, e.g. wearables, sensors
  Standards that enable internet scale - standardised networking, e.g. wifi, 3G, LTE, Bluetooth Smart, browsers, Javascript, HTTP, TLS etc.
  Web and community based development – eco-system enabled by trust, e.g. mbed, HTML5, etc.
  Mobile computing – smart, low-power devices, e.g. smartphones, tablet
Source: ARM training kit

## Slide 17: Technologies that Enable IoT example: ARM-based solutions
Web and community based development
1,000,000s
Platform
Little Devices and Little Data
IEEE 802.15.4
Cortex-M
Devices
Applications
Big Data
Internet of Things
Standards that enable INTERNET scale
LTE
3G
Cortex-A
Mobile Computing
Source: ARM training kit

## Slide 18
End of Session